## Slide 1: Tag-Seq
New RNA-Seq service
Jessica Podnar

## Slide 2: Outline
Overview of RNA-Seq methods
Tag-Seq SOP
Cost Breakdown
Submitting Samples

## Slide 3: RNA-Seq Methods

## Slide 4: RNA-Seq Methods
GSAF has primarily used two methods for RNA-Seq since the introduction of our Illumina Sequencers
  Methods and reagents continue to have slight changes and improvements over time but the concept has not altered
    NEBNext Small RNA kit
      Will be referred to as the sequential ligation based method
    NEBNext Ultra II Directional RNA library kit
      Will be referred to as the dUTP based method
In Addition to these, is the template switching method used to produce RNA-Seq libraries
  This is what we will be referring to as Tag-Seq
    Also known as Switching Mechanism at the 5’ end of the RNA Template (SMART) Clontech
    Capture and Amplification by Tailing and Switching (CATS) Diagenode

## Slide 5: Both the Ligation and dUTP method start with either Poly(A) enrichment or Ribosomal depletion
Image: https://www.thermofisher.com/order/catalog/product/AM1922

## Slide 6: Ligation Based Method

## Slide 7: Ligation Based Method
Input RNA is fragmented
3’ Adapter is ligated onto the RNA (this is the Read 2 portion of the Adapter)
Next is the hybridization of the SR RT Primer
  Note that this is complimentary to the 3’ Adapter, will prevent adapter-dimer formation
  Hybridizes to the 3’ Adapter
5’ Adapter Ligation (this is Read 1 Primer site)
Perform Reverse Transcription, first strand cDNA synthesis
Amplify the cDNA

## Slide 8: Ligation Based Method
Image: https://www.neb.com/products/e7330-nebnext-small-rna-library-prep-set-for-illumina-multiplex-compatible#Product%20Information
PCR cDNA
Input RNA is fragmented

## Slide 9: dUTP Method

## Slide 10: dUTP Method
Starting material again is one of three most popular choices
  Poly(A) enriched RNA, Ribo-Depleted RNA of Total RNA
  First Step is to fragment the RNA
  Next cDNA synthesis, first and second strand
  During second strand synthesis Uracil is incorporated in place of Thymine
  Second strand is now considered “marked”
  The cDNA is then treated with the “USER” enzyme (Uracil-Specific Excision) used to degrade the second strand
  The treatment can happen directly after Adapter ligation of just before to PCR amplification

## Slide 11: dUTP Method
https://www.neb.com/-/media/catalog/Long%20Description/Illumina_UltraNonDirRNAWorkflow_0916.png

## Slide 12: Tag-Seq

## Slide 13: Tag-Seq
R2 Primer Site
R1 Primer Site

## Slide 14
Tag-Seq Library Construction
During first strand synthesis as the
MMLV reaches the 5’ end it intrinsically
adds additional nucleotides
Majority of these nucleotides are deoxycytidine
These nucleotides serve as an anchor
for the switch oligos
NEW SOP introduces 3 oligos at this step
to assist with base diversity
The new cDNA strand with portions of the
adapter add is then amplified
Following cDNA amplification there
is a second PCR to add the index portion
of the adapter
Meyer E., Aglyamova G.V., Matz M.V (2011) Profiling gene expression responses of coral larvae (Acropora millepora)
to elevated temperature and settlement inducers using a novel RNA-Seq procedure, Molecular Ecology 365-294

## Slide 15: Tag-Seq Library Prep
Fragment the RNA
First Strand synthesis
Amplify the cDNA
Add the indices to the cDNA
Pool Samples
Size Select with Pippin
Sequence on a Single End Run

## Slide 16: Swtich Oligo currently being used
swOligo is an DNA-RNA oligo with special isomeric bases at the 5’ end
/5Me-isodC/iisodG/iMe-isodC/CCATGCGGCTACACGACGCTCTTCCGATCTNNMWrGrGrG

## Slide 17: BA Traces on Tag-Seq libraries
Amplified cDNA
Final Library Post Pippin

## Slide 18: Tag-Seq Cost

## Slide 19: Cost Breakdown
Where does the 1/10th of the cost come from? That would be a comparison of the only the reagents. For example the NEBNext UltraII RNA prep kit is $33 a sample and for just the reagents for Tag-Seq it is $2.9 a sample

## Slide 20: Price for Library Prep and Sequencing

## Slide 21: How to Submit Sample
Samples should be submitted in a 96 well plate
Samples should be at a concertation between 10-100 ng/ul
Customer should provide at least 20 ul of RNA
RNA should be clean and free of any contaminants such as ethanol
RNA should be high quality and intact
  GSAF can check the quality in necessary

## Slide 22: Example of Intact and Degraded RNA